## Slide 1
Senior Design I- Spring 2020
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Mixing
Cleaning
Deconstruction
Objective
Future Work
Objective
Senior Design I- Spring 2020
Industry Supporter: Arthur Niemoller, Sven Bader
Faculty Mentor: Dr. Thomas Koch
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Team Members: Rachel Glendenning, Esther Lee, Quentin McCullough, Matt Parise, Andrew Straight
To develop a system and process for cleaning piping that removes and captures corrosion and contaminants using an oxalic acid mixture. The system must also demonstrate complete oxalic destruction.
System Overview
The system will use a mixing, cleaning, and recovery tank placed in a 3’x 4’ area
Testing samples: Uniform size, corroded metal pipe
Oxalic acid destruction methods:
  Ultraviolet light
  H2O2 (Hydrogen Peroxide)
  O3 (Ozone)
All electrical components are connected on a 16-relay module, with Arduino used to control. A control panel will be used to protect against current surges.
  Mechanical valve to ensure mixing is complete before entering piping
Make Up Tank
Cleaning Tank
  To remove metallic scales in pipes
    Agitation, continuous flow, and heating
Design Features:
  Immersion heater
  6 ultrasonic transducers
  Pipe mount
  50 and 200 T-filters to collect metallic scales
  Oxalic acid destruction
    UV Light, ozone, or peroxide
    Fail-safety switch for no UV light exposure
Contact Information
Rachel Glendenning (ME): rglenden@uncc.edu
Esther Lee (MET): elee60@uncc.edu
Quentin McCullough (ME): qmccullo@uncc.edu
Matthew Parise (MET): mparise1@uncc.edu
Andrew Straight (SE): astraigh@uncc.edu
Summer 2020:
Complete electrical control panel design
Start fabrication
Pump and Piping
Fall 2020:
Complete fabrication and assembly
Perform testing to determine optimal
  Oxalic acid concentration
  Agitation time
  Flow rate
  Temperature
  Deconstruction method
Pump
3 Phase, self priming, centrifugal pump
⅛ HP
Max flow rate 10 GPM
Max particle diameter 3/32 inch
To create an oxalic acid and water solution
Design Features:
  3 Gallon Stainless Steel Tank
  1/32 inch wall thickness
  Mechanical valve to ensure mixing is complete before entering piping
Piping
304 Stainless Steel
¼” NPT diameter
7’ of total piping
Fittings and connections coated with pipe sealant
Recovery Tank
Performance Specifications
Electrical
Mixing
Cleaning
Deconstruction

## Slide 2
Mixing
Cleaning
Deconstruction
Objective
Objective
Senior Design I- Spring 2020
Industry Supporter: Arthur Niemoller, Sven Bader
Faculty Mentor: Dr. Thomas Koch
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Team Members: Rachel Glendenning, Esther Lee, Quentin McCullough, Matt Parise, Andrew Straight
To develop a system and process for cleaning piping that removes and captures corrosion and contaminants using an oxalic acid mixture. The system must also demonstrate complete oxalic destruction.
The system will use a makeup, cleaning, and recovery tank placed in a 3’x 4’ area
Testing samples: Uniform size, corroded metal pipe
Oxalic acid destruction methods:
  Ultraviolet light
  H2O2 (Hydrogen Peroxide)
  O3 (Ozone)
Performance Specifications
Mixing
Cleaning
Deconstruction

## Slide 3
Senior Design I- Spring 2020
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Senior Design I- Spring 2020
Industry Supporter: Arthur Niemoller, Sven Bader
Faculty Mentor: Dr. Thomas Koch
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Team Members: Rachel Glendenning, Esther Lee, Quentin McCullough, Matt Parise, Andrew Straight
System Overview
  Mechanical valve to ensure mixing is complete before entering piping
Make Up Tank
Pump and Piping
Pump
3 Phase, self priming, centrifugal pump
⅛ HP
Max flow rate 10 GPM
Max particle diameter 3/32 inch
To create an oxalic acid and water solution
Design Features:
  3 Gallon Stainless Steel Tank
  1/32 inch wall thickness
  Mechanical valve to ensure mixing is complete before entering piping
Piping
304 Stainless Steel
¼” NPT diameter
7’ of total piping
Fittings and connections coated with pipe sealant

## Slide 4
Objective
Senior Design I- Spring 2020
Industry Supporter: Arthur Niemoller, Sven Bader
Faculty Mentor: Dr. Thomas Koch
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Team Members: Rachel Glendenning, Esther Lee, Quentin McCullough, Matt Parise, Andrew Straight
System Overview
  Mechanical valve to ensure mixing is complete before entering piping
Cleaning Tank
  To remove metallic scales in pipes
    Agitation, continuous flow, and heating
Design Features:
  Immersion heater
  6 ultrasonic transducers
  Pipe mount
  50 and 200 T-filters to collect metallic scales

## Slide 5
Objective
Senior Design I- Spring 2020
Industry Supporter: Arthur Niemoller, Sven Bader
Faculty Mentor: Dr. Thomas Koch
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Team Members: Rachel Glendenning, Esther Lee, Quentin McCullough, Matt Parise, Andrew Straight
System Overview
All electrical components are connected on a 16-relay module, with Arduino used to control. A control panel will be used to protect against current surges.
  Mechanical valve to ensure mixing is complete before entering piping
  Oxalic acid destruction
  UV Light, ozone, or peroxide
    Fail-safety switch for no UV light exposure
Recovery Tank
Electrical

## Slide 6
Senior Design I- Spring 2020
Industry Supporter: Arthur Niemoller, Sven Bader
Faculty Mentor: Dr. Thomas Koch
Optimization and Partial Demonstration of Oxalic Acid Dissolution System
Team Members: Rachel Glendenning, Esther Lee, Quentin McCullough, Matt Parise, Andrew Straight
Future Work
  Mechanical valve to ensure mixing is complete before entering piping
Summer 2020:
Complete electrical control panel design
Start fabrication
Fall 2020:
Complete fabrication and assembly
Perform testing to determine optimal
  Oxalic acid concentration
  Agitation time
  Flow rate
  Temperature
  Deconstruction method